## Slide 1: STIMULAN® Frequently Asked Questions
for Distributors (EU)

## Slide 2: FAQs
What supporting data do you have for STIMULAN?
Biocomposites has a range of data including pre-clinical laboratory testing, in-vivo, clinical, in-vitro microbiology and antibiotic elution data. Biocomposites also has numerous case studies that show how STIMULAN transforms outcomes in infected non-unions, osteomyelitis, periprosthetic joint infections and trauma.
What is STIMULAN Rapid Cure indicated for?
Indications for use for STIMULAN can be found in the Instructions for Use (IFU). STIMULAN Rapid Cure is the perfect partner for your infection management strategy. The characteristics of STIMULAN Rapid Cure make it suitable as a carrier material for substances such as antibiotics. It can be used at an infected site for bone and soft tissue implantation and regeneration. It is indicated for use in musculoskeletal defects created by surgery, a cyst, a tumor, osteomyelitis or traumatic injury. STIMULAN Rapid Cure is not intended to provide structural support during the healing process

## Slide 3: FAQs
What is STIMULAN Rapid Cure contraindicated for?
Contraindications for STIMULAN can be found in the Instructions for Use (IFU). These include contraindications for filling defects which are intrinsic to the stability of the bony structure, hypercalcaemia, severe vascular or neurological disease, uncontrolled diabetes, pregnancy, severe degenerative bone disease and uncooperative patients who can’t or won't follow post-operative instructions including individuals who abuse alcohol or drugs.
How long does STIMULAN take to absorb?
STIMULAN is absorbed in approximately 30-60 days when used in accordance with the device labelling. Contributing factors include the vascularity of the surgical site, quantity used and patient health.
Who is using STIMULAN and in which hospitals?
STIMULAN is already used in over 50,000 cases a year. Biocomposites is happy to introduce physicians to an appropriate surgeon if they would like to have a peer to peer conversation.

## Slide 4: FAQs
Can I mix antibiotics with STIMULAN Rapid Cure?
STIMULAN is approved for mixing with vancomycin, gentamicin and tobramycin and can be placed directly into infected and non-infected sites. Please refer to the Instructions for Use (IFU).
Concurrent use of locally administered antibiotics may affect the setting time, absorption characteristics and/or bone formation. Only the antibiotics shown above can be added and the combination with other antibiotics shall be avoided. It is the surgeon/ healthcare professional’s responsibility to give due consideration to the details contained in the medicinal product marketing authorisation in deciding whether it is appropriate for the patient under his/her care. The relevant Summary of Product Characteristics (SmPc) must be consulted. The type and dose of medicinal substance should also be assessed according to the individual patient’s clinical circumstances.
Can STIMULAN Rapid Cure mixed with antibiotics replace I.V. delivery?
STIMULAN Rapid Cure is not intended as a replacement therapy for I.V. antibiotics.

## Slide 5: FAQs
What is the mechanism of release of the antibiotics?
This is an area of ongoing research. However, molecular size, solubility and wound environment all play a role in the release mechanism. It is likely that most antibiotics will be released through a combination of both dissolution and diffusion.
Can I substitute other mixing solutions or add additional solution when preparing STIMULAN Rapid Cure?
You should only use the mixing solutions provided unless mixing with antibiotics stated in the Instructions for Use. Concurrent use of locally administered antibiotics may affect the setting time, absorption characteristics and/or bone formation. Only the antibiotics shown can be added and the combination with other antibiotics shall be avoided. Using alternative mixing solutions and/or adding other substances to the mixture may alter the setting time significantly. Some substances such as bone marrow and blood will prevent the paste from setting.
Can STIMULAN be applied to a wet field?
The device must be implanted where surrounding bone is healthy and vascular but not actively bleeding at time of insertion. Do not irrigate the site following implantation.

## Slide 6: FAQs
Do we have any information on the use of antiseptic solutions, such as Betadine (povidone iodine) or chlorhexidine, used as wound irrigants and their interaction with locally applied antibiotics and STIMULAN?
Laboratory testing has shown that chlorhexidine solution reacts with calcium sulfate producing a crystalline precipitate. Also povidone iodine solution (Betadine) has been shown to react with vancomycin hydrochloride giving a black/slimy precipitate. The clinical effects of these are unknown.
What potential adverse effects may be associated with the implantation of STIMULAN?
Adverse effects for STIMULAN can be found in the IFU. These may include but are not limited to: Inadequate or incomplete bone formation may occur, material sensitivity/allergic reactions, heterotopic ossification, device migration may occur and result in wound drainage, embolism may occur if injecting the device. Renal failure may occur due to concurrent therapies and/or the patient’s medical condition, including implantation into patients who have, or are at risk of impaired renal function. Hypercalcemia, infection and seroma are associated risks. Known risks and potential adverse effects associated with general surgical procedures may also occur.

## Slide 7: FAQs
Can STIMULAN cause an adverse soft tissue response?
As part of a recent study by the University of New South Wales, Australia, a soft tissue inflammatory response to implanted STIMULAN was determined. The study describes a novel small animal model to investigate dead-space management in muscle tissue1. Results from histology and serological analysis indicated no significant unusual inflammatory response to the implanted materials.
Reference: 1. Oliver, R.A., et al., Development of a Novel Model for the Assessment of Dead Space Management in Soft Tissue. PLoS ONE, 2015. 10(8): p. e0136514.
Can surgeons use STIMULAN when the patient has a known sulfonamide allergy?
The Instructions for Use (IFU) does not contraindicate STIMULAN for sulfa allergies.
Does STIMULAN damage articulating surfaces on joint prosthesis?
Biomechanical testing (Pin on Plate) indicates that STIMULAN does not significantly scratch implant grade cobalt chrome and does not lead to increased wear of high-density polyethylene components, when compared to a control with no STIMULAN present.

## Slide 8: FAQs
Will STIMULAN cause heterotopic ossification (HO) in soft tissue?
STIMULAN is an osteoconductive material and is not osteoinductive or osteogenic in nature. Biocomposites has published a range of clinical data indicating a minimal risk of HO if implanted in soft tissue.
Can wound drainage occur with the use of STIMULAN?
Wound drainage may occur with any implanted material. STIMULAN has a low documented occurrence of wound drainage.
It may be attributed to several factors including patient health and surgical methods e.g.
1) Large volumes of STIMULAN beads placed in a concentrated area may cause stretching of the tissue envelope during normal range of motion and leakage at the wound site.
2) Patients with comorbidities have a much greater probability of drainage due to their poor tissue quality, which may not permit a water tight seal.
To reduce the risk of drainage, ensure complete soft tissue coverage and/or containment is achieved.

## Slide 9: FAQs
Why is there so little drainage associated with STIMULAN?
STIMULAN is a pharmaceutical-grade, synthetic calcium sulfate. The physical and chemical properties are tightly controlled through Biocomposites’ patented recrystallisation process to ensure optimum purity. Evidence has shown that STIMULAN is associated with reduced drainage rates when compared to non-synthetic calcium sulfates. Naturally occurring mineral sources of calcium sulfate can contain non absorbing earth impurities, may be of an acidic pH and hydrophobic in nature, and are often linked to significant problems with wound healing and drainage.
What volume and size of beads can be prepared using the STIMULAN bead mat?
The STIMULAN bead mat can be used to prepare 3mm, 4.8mm or 6mm hemispherical beads. A 10cc pack of STIMULAN Rapid Cure will yield 25cc of bead volume. A 10cc pack of STIMULAN Kit will yield 20cc of bead volume.

## Slide 10: FAQs
What is the powder weight of STIMULAN Rapid Cure per cc of paste volume?
The powder weight of STIMULAN Rapid Cure per cc of paste volume is:
  What is the compressive strength of STIMULAN?
STIMULAN Kit/Rapid Cure have been shown to have a ‘wet’ compressive strength (as set at implantation time) of 21 MPa. This helps maintain bead integrity immediately following bead placement. The compressive strength reduces as STIMULAN is absorbed.
Product Mean Compressive Strength (MPa)
STIMULAN Kit 21
STIMULAN Rapid Cure 21

## Slide 11: FAQs
What are the working and setting times of STIMULAN Rapid Cure?
When mixed with the solution provided STIMULAN Rapid Cure (10cc) has the following setting times:
STIMULAN Rapid Cure has a 1-2 minute working time and will set approximately 4 minutes after mixing. Following mixing and application onto the bead mat, allow to set undisturbed for at least 8 minutes prior to release from bead mat.
STIMULAN Rapid Cure is approved for mixing with vancomycin, gentamicin and tobramycin.
STIMULAN Rapid Cure + Vancomycin (1000mg) – sets in 2-5 minutes
STIMULAN Rapid Cure + Gentamicin (240mg in 6ml solution) – sets in 3-5 minutes
STIMULAN Rapid Cure + Tobramycin (240mg in 6 ml solution) – sets in 5-15 minutes

## Slide 12: FAQs
Concurrent use of locally administered antibiotics may affect the setting time, absorption characteristics and / or bone formation. Antibiotics may affect the setting time as exemplified below for 10cc of STIMULAN Rapid Cure. Only the antibiotics shown can be added and the combination with other antibiotics shall be avoided.
It is the surgeon/healthcare professional’s responsibility to give due consideration to the details contained in the medicinal product marketing authorisation in deciding whether it is appropriate for the patient under his/her care. The relevant Summary of Product Characteristics (SmPc) must be consulted. The type and dose of medicinal substance should also be assessed according to the individual patient’s clinical circumstances. Data based on 10cc Stimulan Rapid Cure for a given quantity of substance.

## Slide 13: FAQs
What are the working and setting times of STIMULAN Kit (beads)?
STIMULAN Kit (beads) has a 1-2 minute working time and will set in approximately 8 minutes after mixing. Following mixing and application onto the bead mat, allow to set undisturbed for at least 15 minutes prior to release from bead mat.
What are the working and setting times of STIMULAN Kit (injectable paste)?
STIMULAN Kit (injectable paste) has a 30 second working time prior to injection and begins to set 2-3 minutes after mixing. Following mixing and application, allow paste to set undisturbed for at least 15 minutes prior to closure.

## Slide 14: FAQs
How does STIMULAN compare to OSTEOSET™?
STIMULAN is the only calcium matrix approved for use in bone and soft tissue and approved for mixing with vancomycin, gentamicin and tobramycin. STIMULAN can be placed directly into infected and non-infected sites and is fully absorbable. OSTEOSET™ can be used at infected sites. It contains non-absorbable impurities and may not fully absorb. OSTEOSET™ is contraindicated in articulating surfaces and may cause third body damage. OSTEOSET™ contains 1.5% stearic acid as an excipient. No universal bead mat is available. OSTEOSET® T (approx. 4% Tobramycin Sulfate) is supplied as preformed pellets only.
How does STIMULAN compare to PerOssal®?
STIMULAN is the only calcium matrix approved for use in bone and soft tissue and approved for mixing with vancomycin, gentamicin and tobramycin. STIMULAN can be placed directly into infected and non-infected sites and is fully absorbable. PerOssal® may be used where infection is present or likely to occur with simultaneous stimulation of bone growth. It is only available in pre-formed beads consisting of hydroxapatite (HA) and calcium sulfate dihydrate. HA may present a third body damage risk. PerOssal® is not intended or cleared for soft tissue.

## Slide 15: FAQs
How does STIMULAN compare to Herafill® Beads G?
STIMULAN is the only calcium matrix approved for use in bone and soft tissue and approved for mixing with vancomycin, gentamicin and tobramycin. STIMULAN can be placed directly into infected and non-infected sites and is fully absorbable. Herafill® beads G are a resorbable bone graft material containing gentamicin sulfate as a protection against bacterial colonisation. The beads are biodegraded completely in bone tissue within a few months. Beads must not be used at the surface of joints.
How does STIMULAN differ from an antibiotic loaded spacer?
STIMULAN is a void filler and the characteristics of STIMULAN make it suitable as a carrier material for substances such as antibiotics. STIMULAN is absorbed over 30-60 days and is therefore not suitable for load bearing. An antibiotic loaded spacer is a device placed into the joint to maintain normal joint space and alignment. Spacers are made with bone cement and loaded with antibiotics. The cement does not get absorbed by the body and therefore needs to be removed during revision surgery.

## Slide 16: FAQs
For any other questions please contact:
    Ian Pass, Senior Marketing Manager, Content - ijp@biocomposites.com
Company Confidential.
  This material is intended for use by Biocomposites' employees and their authorised representatives. This material is for informational purposes only, not for clinical application. Do not copy.
  For indications, contraindications, warnings and precautions see Instructions for Use. Concurrent use of locally administered antibiotics may affect setting time, absorption characteristics and/or bone formation. It is the surgeon/healthcare professional’s responsibility to give due consideration to the details in the medicinal product marketing authorization in deciding whether it is appropriate for the patient under his/her care. The relevant Summary of Product Characteristics (SmPC) must be consulted. The type and dose of medicinal substance should also be assessed according to the individual patient’s clinical circumstance.
  This brochure may include the use of STIMULAN or techniques that go beyond the current clearance / approval granted by the relevant regulatory authority. Please contact your local representative for further information.
  ©2021, Biocomposites, STIMULAN, Bringing Calcium to Life, Power to Transform Outcomes and DRy26 are trademarks/registered trademarks of Biocomposites Ltd. All rights reserved. No unauthorised copying, reproduction, distributing or republication is allowed unless prior written permission is granted by the owner, Biocomposites Ltd.
  Patents granted: GB2367552, EP 1204599 B1, US 6780391, EP 2594231 B1, US 8883063, CN ZL201210466117.X, GB2496710, EP 3058899 B1, US 10390954, US 10,588,748, CN ZL201610089710.5
  Patents pending: GB1502655.2, GB1704688.9, EP 18275044.8, US 15/933936, CN 108619579A
  MA0036R5